ASEM Printer

Windows Driver & Installer

User Guide

Unless otherwise specified, the document is printed or copied document are not controlled

Contents

Chapter 1: Getting Started

Overview

Operating Environment

Requirements

Preparations

Chapter 2: Installation of Printer

Verify interface type of printer

Installing a Serial printer

Installing an USB printer

Installing an USB to serial printer

Installing an Ethernet printer

Checking installed printer

Chapter 3: Uninstallation of Printer

Uninstalling a printer

Chapter 4: Specifications of Printer

Printer fonts

Printer resolutions & Paper sizes

Chapter 5: Properties of Printer

Printer device control

Additional configurations

Chapter 6: Trouble Shooting

Installation troubleshooting

Uninstallation troubleshooting

Printing troubleshooting

Appendix : Testing for Printer Driver using the WordPad

Getting Started

Overview

This document contains how to install/uninstall a printer with an interface and contains how to configure a printer.

To install a printer, refer follows:

- Install proper printer driver.

- In case of a serial printer (p.6).

- In case of an USB printer (p.9).

- In case of an USB to serial printer (p.14).

- In case of an Ethernet printer (p.19).

- Make sure installed printer is properly works (p.21).

To uninstall a printer, refer (p.24).

Operating Environment

| X86 (32bit) | WEPOS, POSReady2009, Windows XP Pro, Windows Vista, Windows 7, Windows 8 |
| --- | --- |
| X64 (64bit) | Windows XP Pro, Windows Vista, Windows 7, Windows 8 (WEPOS, POSReady2009 doesn’t provide the x64) |

Requirements

Warning: This requirement should be satisfied for using a printer.

* To install/uninstall a printer, ‘.Net framework 3.0’ or above should have installed.

* To install a printer properly, please make sure any related hardware works fine and interface of printer is well connected.

Preparations

Preparations for using the windows driver installer:

- Double click the provided executable file so that files for the windows driver installer is extracting to ‘Program Files\ASEM PrinterDriver’ folder for a 32bit OS.

For a 64bit OS, the files are extracting to ‘Program Files [x86]\ASEM PrinterDriver’ folder.

- This executable file is the ‘WinRAR 32bit executable-extracting’ file so compatibility message can be displayed on a 64bit OS.

If following message is shown, click ‘This program installed correctly’ to progress that will not affect any program or system.

- The windows driver installer will be started automatically after extracting files.

- You can execute the printer driver installer through shortcut that is on the ‘Program Menu’.

Please refer below for detail.

Installation of Printer

Verify interface type of Printer

Checks interface of printer from the ‘self-test’. The self-test checks the following:

- Make sure paper roll has been installed properly.

- Turn on the power while holding down the FEED button. The self-test begins.

- The self-test prints the current printer status, which provides the control ROM version and the printer setting.

- After printing the current printer status, self-test printing will print the following and pause (The paper LCD / the LCD light blinks).

- Press the FEED button to continue printing. The printer prints a pattern using the built-in character set.

- The self-test automatically ends and cuts the paper after printing the following.

- The printer is ready to receive data as soon as it completes the self-test.

- You can find interface type of printer from the self-test as following.

- Interface list

USB-I INTERFACE for ‘SERIAL /VCOM CONNECTION’

USB-II INTERFACE for ‘USB CONNECTION’

PARALLEL INTERFACE for ‘PARALLEL CONNECTION’

Ethernet-II INTERFACE for ‘ETHERNET CONNECTION’

WIRELESS LAN (WLAN) INTERFACE for ‘ETHERNET CONNECTION’

SERIAL (RS-232C) INTERFACE - 25 pin for ‘SERIAL /VCOM CONNECTION’

SERIAL/WIRELESS INTERFACE - 9 pin for ‘SERIAL /VCOM CONNECTION’

Installing a Serial printer

- Selecting a printer that will be installed.

- Selecting the ‘SERIAL / VCOM CONNECTION’.

3. Selecting a port.

- If you don’t have a serial port on your system, you can’t progress further. For solution of this issue, please refer p.34.

- Configuring the selected port.

- Confirming installation.

- Installation completed.

Installing an USB printer

Warning: Before finishing installation of USB printer, printer should not be connected with PC

- Selecting a printer that will be installed.

- Selecting the ‘USB CONNECTION’.

- Confirming installation.

- Confirming security check.

- In case of windows XP

- In case of windows vista or above

- Once you check the ‘Always trust software …’ and click the install, the Windows Security message will not display any more.

- Driver installation completed.

- Connecting printer so that the printer is installing.

- In case of windows XP

- Notification of connection.

- Hardware Wizard for the USB.

- Installation complete.

- In case of windows vista or above

- Notification of connection.

OS will setup the printer automatically.

- Installation complete.

Installing an USB to serial printer

Warning: Before finishing installation of printer, printer should not be connected with PC

- Selecting a printer that will be installed.

- Selecting the ‘SERIAL / VCOM CONNECTION’.

- Selecting a port.

- If you already installed USB to serial driver, you can select the installed port for printer driver.

- Configurations of selected port.

- Confirming installation.

- Installation completed.

- Connecting printer so that ‘USB to serial’ interface is installing.

- In case of windows XP

- Notification of connection.

- Hardware Wizard for the USB.

- Installation for ‘USB to serial’ is completed.

- In case of windows vista or above

- Notification of connection.

- OS will setup the ‘USB To Serial’ interface automatically.

- Checking the installed port of ‘USB To Serial’ from Device Control.

- Restart system to complete installation of ‘USB to serial’ port.

- Open properties of installed printer.

- Changing port that is checked from step 8 by clicking name of port.

- Installation Completed.

Installing an Ethernet printer

- Selecting a printer that will be installed.

- Selecting the ‘ETHERNET CONNECTION’.

- Configuration for TCP/IP.

- Default Port of printer: 6001

- Confirming installation.

- Installation completed.

Checking installed printer

- Checking installed printer.

- In case of Windows XP.

- In case of Windows Vista or above.

- Verifying properties that are ‘Driver’ and ‘Print Processor’ of installed printer from the Advance tap.

- Printing test page from the General tap and checking the printed paper.

Uninstallation of Printer

Uninstalling printer(s)

.

- There is two ways to start uninstallation.

- Starting from ‘Add or Remove Program’.

- Starting from ‘Program Menu’.

- If there is an installed printer, printer installation / Uninstallation can make a choice.

‘Printer Uninstall’ is selected as the default setting if you have an installed printer. If the printer installer doesn’t show the dialog despite you have an installed printer, please refer p.38.

Selecting the ‘ASEM PRINTER UNINSTALL’.

- Selecting one or more printer that will be uninstalled.

- Confirming uninstallation.

- Uninstallation completed.

Specifications of Printer

Printer fonts

These drivers support use of printer fonts as well as Windows fonts. Use of printer fonts permits faster printing. Available printer fonts are listed below.

“Built-in fonts of a printer” can be specified with the application programs. The “built-in fonts” are as follows.

- Printer Font (type A, Large)

- Printer Font (type B, Small)

The font names what the user can choose in to the application are as follows. 2 types of character-height can be chosen in each font. They are two kinds of the FontAXxX (Ext.) font and the FontAXxX. The character code of 128 bytes of 80H - FFH varies in the difference in these printer fonts. A FontAXxX font supports ANSI character code (Code Page 2: 850). And, a FontAXxX (Ext.) font supports IBM expansion character code (Code Page 0: 437). A FontAXxX (255) font supports space page. (Code Page: 255).

Printer can be used to execute a variety of special non-printing functions, as indicated in the table below. You can execute these functions by selecting the printer’s special “FontControl” font and then sending the appropriate character code to the driver. (Note that you cannot use the “FontControl” font to print normal characters)

| Character | Special Function |  |
| --- | --- | --- |
| 5 | HT is output |  |
| 6 | LF is output |  |
| 7 | CR is output |  |
| a | Open Drawer 2 (50ms drive pulse width) |  |
| b | Open Drawer 2 (100ms drive pulse width) |  |
| c | Open Drawer 2 (150ms driver pulse width) |  |
| d | Open Drawer 2 (200ms drive pulse width) |  |
| e | Open Drawer 2 (250ms drive pulse width) |  |
| g | Cut Receipt (partial cut) without paper feeding |  |
| p | HRI characters are not added to the bar code |  |
| q | HRI character are added at the top of the bar code using Font A |  |
| r | HRI characters are added at the bottom of the bar code using Font A |  |
| s | HRI characters are added at the top of the bar code using Font B |  |
| t | HRI characters are added at the bottom of the bar code using Font B |  |
| w | Text is aligned left |  |
| x | Text is centered |  |
| y | Text is aligned right |  |
| A | Open Drawer 1 (50ms drive pulse width) |  |
| B | Open Drawer 1 (100ms drive pulse width) |  |
| C | Open Drawer 1 (150ms driver pulse width) |  |
| D | Open Drawer 1 (200ms drive pulse width) |  |
| E | Open Drawer 1 (250ms drive pulse width) |  |
| G | NV bit image No 1 is printed in the Normal mode |  |
| H | NV bit image No 2 is printed in the Normal mode |  |
| I | NV bit image No 3 is printed in the Normal mode |  |
| J | NV bit image No 4 is printed in the Normal mode |  |
| K | NV bit image No 5 is printed in the Normal mode |  |
| P | Cut Receipt (partial cut) |  |
| [ | NV bit image No 1 is printed in the Double Height Double Width mode |  |
| ] | NV bit image No 2 is printed in the Double Height Double Width mode |  |
| ^ | NV bit image No 3 is printed in the Double Height Double Width mode |  |
| _ | NV bit image No 4 is printed in the Double Height Double Width mode |  |
| ` | NV bit image No 5 is printed in the Double Height Double Width mode |  |

Printer resolutions & Paper sizes

- Resolutions

The resolution setting supported is 180 x 180.

- Paper sizes

The paper sizes supported are as follow.

- 80 x 3279 mm

- 80 x 297 mm

- 80 x 200 mm

- 80 x 160 mm

- 80 x 120 mm

- 80 x 80 mm

- 80 x 40 mm

- 58 x 3276 mm

- 58 x 297 mm

The following table shows the recommended margins for ASEM printer. Refer to this table when setting margins from your printing applications.

| Printer | Margins | Printer Area |
| --- | --- | --- |
|  | Left[mm] | Right[mm] | Top[mm] | Bottom[mm] | Width[mm] |
| ASEM printer | 0 | 0 | 0 | 0 | 80 |

Properties of Printer

Printer device control

- You can be entered a command you wanted to at the point of starting document.

Ex) \x1B\x70\x00\x19\xff = Open Drawer 1 (50ms drive pulse width)

- You can fire cash drawer 1 or 2.

- You can be entered a command you wanted to at the point of ending page.

Ex) \x1D\x56\x42 = Cut Receipt, Type the command to cut.

- This is where you enter the number of line feeds that will be done after a document is printed.

- You can fire cash drawer 1 or 2.

Additional configurations

- Configuration for printer copies

Printers provide three options for printer copies.

- Number of print copies.

- Paper cut option.

Checking this option will execute paper cut per each copies.

- Cash drawer fire option.

Checking this option will fire cash drawer per each copies.

- Configurations for printer papers.

Printers provide the ‘Add New paper Size’ button for creating a custom paper size and modifying a paper size.

Clicking the button will open the ‘Custom Paper Size’ dialog.

- You can add or modify a paper form. The paper properties must be filled.

If you want to make a new paper size, file the ‘Form Name’ that is not on the list and fill the paper size properties.

- You can delete a selected paper form.

- If you select an item from the list, paper properties of selected item that is a paper form will be filled automatically.

You can modify or delete the selected item.

Trouble Shooting

Installation troubleshooting

- Not found a serial port.

If you don’t have a serial port on your system, Installation for serial port is not possible.

What you need to do is make sure whether system has a serial port or not from the ‘Device Manager’

- Scanning for hardware to make sure all of hardware is installed.

- Checking ‘COM (communications) Port’ on the list.

- If you don’t have any ‘COM Port’ on the list, please ask assistance to hardware engineer of your system.

- Not found a USB to serial port.

If you don’t have a serial port including USB to serial port on your system, Installation for serial port is not possible.

What you need to do is make sure whether system has a USB to serial port or not from the ‘Device Manager’

- Scanning for hardware to make sure all of hardware is installed.

- Checking ‘COM (communications) Port’ on the list.

- If you don’t have any ‘USB to serial Port’ on the list, please refer ‘Installing USB to serial printer’ (p.14) to install a USB to serial printer.

- If you have ‘USB to serial Port’ on the list but the printer installer doesn’t show the port when you install a printer, please re-boot your system to apply changes completely and try again.

Uninstallation troubleshooting

- Unable to uninstall.

- Make sure a printer is installed from the ‘Printers and Faxes’.

- In case of Windows XP.

- In case of Windows Vista or above.

- If the list of ‘Printers and Faxes’ is not shown, execute ‘net start spooler’ from the ‘Run’.

To open ‘Run’ dialog, press the ‘Windows Key’ with ‘R Key’.

- Uninstalling the Printer Driver Installer.

- Delete the installer files:

32bit OS ( Root\Program Files\ASEM PrinterDriver

64bit OS ( Root\Program Files(x86)\ASEM PrinterDriver

- Delete the shortcut of the installer.

Printing troubleshooting

- If printing for a document is not properly.

Open the ‘Printer properties’ from the ‘Printers and Faxes’.

- In case of Windows XP.

- In case of Windows Vista or above.

- Verifying properties that are ‘Driver’ and ‘Print Processor’ of installed printer from the ‘Advance’ tap.

If the Print Processor is assigning the ‘winprint’, select the ‘ASEM SR80’.

- If installed printer doesn’t show on the list of printers.

- Make sure a printer is installed from the ‘Printers and Faxes’.

- In case of Windows XP.

- In case of Windows Vista or above.

- If the list of ‘Printers and Faxes’ is not shown, execute ‘net start spooler’ from the ‘Run’.

To open ‘Run’ dialog, press the ‘Windows Key’ with ‘R Key’.

APPENDIX							: Testing for printer driver using the WordPad

## WordPad Environment

WordPad is more adequate to test printer than Microsoft Word. Make it sure that ASEM Printer has been chosen as default printer and then go further with WordPad like below.

- Size		[Refer to Section 4.5, “Paper Sizes”]

- Resolution	[Refer to Section 4.4, “Resolutions”]

- Margins	[Refer to Section 4.5, “Paper Sizes”]

## Printing Text

1. Select the font you wish to use from the font list.

2. Select the font size you wish use from the font-size list.

3. Type in some text into the WordPad text-input area.

4. Open the File menu, and click on Print.

* For fastest printing, select a printer font form the font list.

## Opening the Cash Drawer

1. Select the “FontControl” font from the font list.

2. Set the font size to 10.

3. Type an “A” into the WordPad text-input area.

4. Open the File menu, and click on Print.

* Clicking on Print will cause cash drawer #1 to open at a drive speed of 50ms. By changing the character that you input at Step 3, you can select different driver speed or open the other drawer.

## Cutting the Paper

1. Select the “FontControl” font from the font list.

2. Set the font size to 10.

3. Type in “P”.

4. Open the File menu, and click on Print.

## Bar Code Printing

1. Select the “Code128”font from the font list.

2. Set the font size to 10.

3. Type in an “{A123545”

4. Open the File menu, and click on Print.

# Text boxes

1

2

3

4

5

1

2

3

4

5

1

3

2

6